## Slide 1: Assembly Language
Part II Assembly Language Syntax and Program Data
Department of Computer Science, Faculty of Science, Chiang Mai University

## Slide 2: Outline
Statements
Program Data
Variables
Named Constants
Basic Instructions
Translation of High-Level Language to Assembly Language

## Slide 3: Assembler
Assembly language programs are translated into machine language instructions by an assembler,
In an assembly language program we may express data as binary, decimal, or hex numbers, and even as characters.

## Slide 4: Instruction
It is translated into machine code by the assembler.
name operation operand(s) comment
START: MOV CX, 5 ; initialize counter

## Slide 5: Assembler Directive
It instructs the assembler to perform some specific tasks. such as allocating memory space for a variable or creating a procedure.
MAIN PROC

## Slide 6: Name Field
The name field is used for instruction labels, procedure names, and variable names.
The assembler translates names into memory addresses.
Names can be from 1 to 31 characters long. and may consist of letters, digits, and the special characters ? . @ _ $ %.

## Slide 7: Name Field
Embedded blanks are not allowed.
If a period is used, it must be the first character.
Names may not begin with a digit.
The assembler does not differentiate between upper and lower case in a name.

## Slide 8: Examples of Legal Names
COUNTER1
@character
SUM_OF_DIGITS
$1000
DONE?
.TEST

## Slide 9: Examples of Illegal Names
TWO WORDS contains a blank
2abc begins with a digit
A45.28 . not first character
YOU&ME contains an illegal character

## Slide 10
Number Type
11011 Decimal
11011B Binary
64223 Decimal
-21843D Decimal
1,234 Illegal
1B4DH Hex
1B4D Illegal Hex Number
FFFFH Illegal Hex Number
0FFFFH Hex

## Slide 11: Characters
Characters and strings must be enclosed in single or double quotes.
"A" or 'hello'
Characters are translated into their ASCII codes by the assembler, so there is no difference between using "A" and 41h in a program.
"A" = 41h

## Slide 12
Data-defining Pseudo-op Stands for
DB Define Byte
DW Define Word
DD Define Doubleword
DQ Define Quadword
DT Define Tenbytes

## Slide 13: Byte Variables
name DB initial_value
ALPHA DB 4
BYT DB ?
[-128, 127] for signed interpretation
[0, 255] for unsigned interpretation

## Slide 14: Word Variables
name DW initial_value
WRD DW -2
[-32768, 32767] for signed interpretation
[0, 65535] for unsigned interpretation

## Slide 15: Arrays
B_ARRAY DB 10H, 20H, 30H
Symbol Address Contents
B_ARRAY 0200h 10h
B_ARRAY+1 0201h 20h
B_ARRAY+2 0202h 30h

## Slide 16: Arrays
W_ARRAY DW 1000,40,29887,329
Symbol Address Contents
W_ARRAY 0300h 1000d
W_ARRAY+2 0302h 40d
W_ARRAY+4 0304h 29887d
W_ARRAY+6 0306h 329d

## Slide 17: High and Low Bytes of a Word
WORD1 DW 1234H
The low byte of WORD1 contains 34h, and the high byte contains 12h.
The low byte has symbolic address WORD1, and the high byte has symbolic address WORD1+1.

## Slide 18: Character Strings
LETTER DB ‘ABC’
LETTER DB 41H, 42H, 43H
MSG DB ‘HELLO’, 0AH, 0DH, ‘$’
MSG DB 48H, 45H, 4CH, 4CH, 4FH, 0AH, 0DH, 24H

## Slide 19: EQU
The EQU (equates) pseudo-op is used to assign a name to a constant.
name EQU constant
LF EQU 0AH
MOV DL, 0AH
MOV DL, LF
PROMPT EQU ‘TYPE YOUR NAME’
MSG DB ‘TYPE YOUR NAME’
MSG DB PROMPT

## Slide 20: MOV
The MOV instruction is used to transfer data between registers, between a register and a memory location, or to move a number directly into a register or memory location.
MOV destination, source
MOV AX, WORD1
MOV AX, BX
MOV AH, ‘A’

## Slide 21: XCHG
The XCHG operation is used to exchange the contents of two registers, or a register, and a memory location.
XCHG destination, source
XCHG AH, BL
XCHG AX, WORD1

## Slide 22: Legal Combinations of Operands for MOV
 | Destination Operand |  |  | 
Source Operand | General Register | Segment Register | Memory Location | Constant
General Register | Yes | Yes | Yes | No
Segment Register | Yes | No | Yes | No
Memory Location | Yes | Yes | No | No
Constant | Yes | No | Yes | No

## Slide 23: Legal Combinations of Operands for XCHG
 | Destination Operand | 
Source Operand | General Register | Memory Location
General Register | Yes | Yes
Memory Location | Yes | No

## Slide 24: Restrictions on MOV and XCHG
ILLEGAL: MOV WORD1, WORD2
MOV AX, WORD2
MOV WORD1, AX

## Slide 25: ADD and SUB
The ADD and SUB instructions are used to add or subtract the contents of two registers, a register and a memory location, or to add (subtract) a number to (from) a register or memory location.
ADD destination, source
SUB destination, source
ADD WORD1, AX
SUB AX, DX
ADD BL, 5

## Slide 26: Legal Combinations of Operands for ADD and SUB
 | Destination Operand | 
Source Operand | General Register | Memory Location
General Register | Yes | Yes
Memory Location | Yes | No

## Slide 27: Restrictions on ADD and SUB
ILLEGAL: ADD BYTE1, BYTE2
MOV AL, BYTE2 ; AX gets BYTE2
ADD BYTE1, AL ; add it to BYTE1

## Slide 28: INC
INC (increment) is used to add 1 to the contents of a register or memory location.
INC destination
INC WORD1

## Slide 29: DEC
DEC (decrement) subtracts 1 form a register or memory location.
DEC destination
DEC BYTE1

## Slide 30: NEG
NEG is used to negate the contents of the destination.
NEG does this by replacing the contents by its two’s complement.
NEG destination
NEG BX

## Slide 31: Type Agreement of Operands
MOV AX, BYTE1 ; illegal
MOV AH, ‘A’
MOV AX, ‘A’ ; move 0041h into AX

## Slide 32: Translation of High-Level Language to Assembly Language
Statement Translation
B = A MOV AX, A ; move A into AX
MOV B, AX ; and then into B

## Slide 33: Translation of High-Level Language to Assembly Language
Statement Translation
A = 5 – A MOV AX, 5 ; put 5 in AX
SUB AX, A ; AX contains 5 – A
MOV A, AX ; put it in A

## Slide 34: Translation of High-Level Language to Assembly Language
Statement Translation
A = 5 – A NEG A ; A = –A
ADD A, 5 ; A = 5 – A

## Slide 35: Translation of High-Level Language to Assembly Language
Statement Translation
A = B – 2 x A MOV AX, B ; AX has B
SUB AX, A ; AX has B – A
SUB AX, A ; AX has B – 2 x A
MOV A, AX ; move result to A

## Slide 36: Reference
Ytha Yu and Charles Marut, Assembly Language Programming and Organization of the IBM PC. New York: McGraw-Hill, 1992.