## Slide 1: Assembly Language
Part IV The FLAGS Register
Department of Computer Science, Faculty of Science, Chiang Mai University

## Slide 2: Outline
The FLAGS Register
Overflow
How Instruction Affect the Flags

## Slide 3: FLAGS

## Slide 4: The Status Flags
The processor uses the status flags to reflect the result of an operation.
The status flags are located in bits 0, 2, 4, 6, 7, and 11.

## Slide 5: Carry Flag (CF)
CF = 1 if there is a carry out of msb on addition, or there is a borrow into msb on subtraction; otherwise, CF = 0.

## Slide 6: Parity Flag (PF)
PF = 1 if the low byte of a result has an even number of one bits (even parity).
PF = 0 if the low byte has odd parity.

## Slide 7: Auxiliary Carry Flag (AF)
AF = 1 if there is a carry out from bit 3 on addition, or a borrow into bit 3 on subtraction.

## Slide 8: Zero Flag (ZF)
ZF = 1 for a zero result.
ZF = 0 for a nonzero result.

## Slide 9: Sign Flag (SF)
SF = 1 if the msb of a result is 1; it means the result is negative if you are giving a signed interpretation.
SF = 0 if the msb is 0.
SF = MSB

## Slide 10: Overflow Flag (OF)
OF = 1 if signed overflow occurred, otherwise OF = 0.

## Slide 11: Decimal Range
UNSIGN SIGN
BYTE [0, 255] [-128, 127]
WORD [0, 65535] [-32768, 32767]

## Slide 12: Overflow
No Overflow
Signed Overflow Only
Unsinged Overflow Only
Both Overflows

## Slide 13: The Example of Unsigned Overflow
ADD AX, BX
1111 1111 1111 1111 65535 AX = FFFFh
+ 0000 0000 0000 0001 1 BX = 0001h
1 0000 0000 0000 0000 00000 AX = 0000h
1 0000 0000 0000 0000 = 65536 > 65535

## Slide 14: The Example of Signed Overflow
ADD AX, BX
0111 1111 1111 1111 32767 AX = 7FFFh
+ 0111 1111 1111 1111 32767 BX = 7FFFh
1111 1111 1111 1110 -2 AX = FFFEh
32767 + 32767 = 65534 <> -2

## Slide 15: How the Processor Determines that Unsigned Overflow Occurred
CF = 1
Addition
  There is a carry out of the msb.
  The correct answer is larger than the biggest unsigned number (FFFFh and FFh).
Subtraction
  There is a borrow into the msb.
  The correct answer is smaller than 0.

## Slide 16: How the Processor Determines that Signed Overflow Occurred
OF = 1
  There is a carry into the msb but no carry out.
  There is a carry out but no carry in.
Addition
  The sum has a different sign.
Subtraction
  The result has a different sign than expected.
  A – (–B) = A + B
  –A – (+B) = –A + –B
Addition of Numbers with Different Signs
  Overflow is impossible.
  A + (– B) = A – B

## Slide 17: How Instructions Affect the Flags
Instruction Affects Flags
MOV/XCHG none
ADD/SUB all
INC/DEC all except CF
NEG all (CF = 1 unless result is 0,
OF = 1 if word operand is 8000h,
or byte operand is 80h)

## Slide 18: ADD AX, BX where AX contains FFFFh and BX contains FFFFh.
FFFFh 1111 1111 1111 1111
+ FFFFh + 1111 1111 1111 1111
1 FFFEh 1 1111 1111 1111 1110 AX = FFFEh
SF = 1 because the msb is 1.
PF = 0 because there are 7 (odd number) of 1 bits in
the low byte of the result.
ZF = 0 because the result is nonzero.
CF = 1 because there is a carry out of the msb on addition.
OF = 0 because the sign of the stored result is the same as that of the numbers being added (as a binary addition, there is a carry into the msb and also a carry out).

## Slide 19: ADD AL, BL where AL contains 80h and BL contains 80h.
80h 1000 0000
+ 80h + 1000 0000
1 00h 1 0000 0000 AL = 00h
SF = 0 because the msb is 0.
PF = 1 because all the bits in the result are 0.
ZF = 1 because the result is 0.
CF = 1 because there is a carry out of the msb on addition.
OF = 1 because the numbers being added are both negative,
but the result is 0 (as a binary addition, there is
no carry into the msb but there is a carry out).

## Slide 20: SUB AX, BX where AX contains 8000h and BX contains 0001h.
8000h 1000 0000 0000 0000
– 0001h – 0000 0000 0000 0001
7FFFh 0111 1111 1111 1111 AX = 7FFFh
SF = 0 because the msb is 0.
PF = 1 because there are 8 (even number) one bits in the low byte of
the result.
ZF = 0 because the result is nonzero.
CF = 0 because a smaller unsigned number is being subtracted from
a larger one.
OF = 1 because in a signed sense we are subtracting a positive number
from a negative one, which is like adding two negatives but
the result is positive (the wrong sign).

## Slide 21: INC AL where AL contains FFh.
FFh 1111 1111
+ 1h + 0000 0001
1 00h 1 0000 0000 AL = 00h
SF = 0, PF = 1, ZF = 1.
CF is unaffected by INC.
If CF = 0 before the execution of the instruction, CF will still be 0 afterward.
OF = 0 because numbers of unlike sign are being added (there is a carry into the msb and also a carry out).

## Slide 22: MOV AX, -5
AX = FFFBh
None of the flags are affected by MOV.

## Slide 23: NEG AX where AX contains 8000h.
8000h = 1000 0000 0000 0000
one’s complement = 0111 1111 1111 1111
+1
= 1000 0000 0000 0000 = 8000h
SF = 1, PF = 1, ZF = 0.
CF = 1 because for NEG CF is always 1 unless the result is 0.
OF = 1 because the result is 8000h; when a number is
negated, we would expect a sign change, but because
8000h is its own two’s complement, there is no
sign change.

## Slide 24: Reference
Ytha Yu and Charles Marut, Assembly Language Programming and Organization of the IBM PC. New York: McGraw-Hill, 1992.