## Slide 1: Assembly Language
DEBUG
Department of Computer Science, Faculty of Science, Chiang Mai University

## Slide 2: The DEBUG Program
The DEBUG program provides an environment in which a program may be tested.
The user can step through a program, and display and change the registers and memory.
We use DEBUG to demonstrate the way instructions affect the flags.
To enter DEBUG with our demonstration program, we type
  C:\DEBUG filename.exe

## Slide 3: DEBUG Commands
R display registers
T trace the instruction at CS:IP
G execute at CS:IP to completion
U unassembled data in instruction format
D dump bytes in hex format
E enter data in list beginning at start
Q quit DEBUG and return to DOS

## Slide 4: R
R Display registers and flags
RAX Display AX and change contents if desired
- R
AX=FFFF BX=0000 CX=0019 DX=0000 SP=0100 BP=0000 SI=0000 DI=0000
DS=06BA ES=06BA SS=06CC ​​CS=06CA IP=0000 NU UP EI PL NZ NA PO NC
06CA:0000 BBCBO6 MOV AX, 06CB
Flags
Machine Code
Segment : Offset

## Slide 5
FLAG CLEAR (0) SYMBOL SET (1) SYMBOL
Overflow Flag NV (no overflow) OV (overflow)
Direction Flag * UP (up) DN (down)
Interrupt Flag * DI (disable interrupt) EI (enable interrupts)
Sign Flag PL (plus) NG (negative)
Zero Flag NZ (nonzero) ZR (zero)
Auxiliary Carry Flag NA (no auxiliary carry) AC (auxiliary carry)
Parity Flag PO (odd parity) PE (even parity)
Carry Flag NC (no carry) CY (carry)
* Control Flags

## Slide 6: Reference
Ytha Yu and Charles Marut, Assembly Language Programming and Organization of the IBM PC. New York: McGraw-Hill, 1992.